## Slide 1: NA61 Readout Upgrade based on the DRS

## Slide 2: Overview
DRS initially proposed as replacement for ToF readout
DRS ~= sampling ADC ~= 5 GHz waveform digitizer
very flexible readout system, originally designed for very fast signals like PMTs,
but can be used for a variety of detectors and applications
DRS can be used to upgrade the readout of different NA61 subsystems:
ToF (add multihit capabilities … )
PSD (analysis of waveforms … )
“beam” (not all beam counters readout with TDCs, add multihit …)
BPD (add timing information to beam tracks ~ Dt ~ 10 nsec …)
i.e. replace all old electronics
combine discriminator (CFD), ADC (multihit !), and TDC (multihit !) in a single module
i.e. remove CFDs, splitters, TDCs, ADCS, …
add multihit capabilities

## Slide 3: Waveforms
BPD signlas
FWHM ~ 120 ns
-> slow digitization
ToF-L signals
risetime ~ 3 ns
-> fast digitization

## Slide 4: How to Measure Best Timing (1)
basically two options:
1. (CF) discriminator + multihit TDC
2. waveforme digitizer (flash ADC + FPGA)
the waveforme approach combines different functionalities with no D.T.:
discriminator, multi-hit TDC, Q-ADC, peak-sensing ADC, etc.
PROBLEM : 10(0) ps resolution requires very high sampling rate > 1 GHz
amplifier ~10x
discriminator
(const fract)
multihit TDC
25 ps res.
deep buffer
~ 25 bit encoding
optical link
10 kHz readout
Si-PM
amplifier ~10x
flash ADC
< 1 GHz
10 -12 bit
FPGA
same frequency
CFD algorithm
(real time)
optical link
continuous readout
Si-PM

## Slide 5: How To Measure Best Timing (2)
J.-F. Genat et al., NIM A607 (2009) 386
D. Breton et al., NIM A629 (2011) 123
simulation of MCP PMT
with realistic noise and best discriminators
Beam measurements
@ SLAC and FNAL
17 ps (s) can be achieved with waveform digitizing and 40 photoelectrons

## Slide 6: Digital Constant Fraction Discriminator
Delayed
signal
Inverted
signal
Sum
Latch
Latch
Latch
Latch
Latch
12 bit
Clock
S
+
+
MULT
Latch
0
&
<0
t
¼ max ampli
simpler CFD version
200 ps sampling
without doing nothing
-> 200 ps / sqrt(12) ~ 60 ps
with interpolation
expect 5 x better
performance

## Slide 7: DRS “Philosophy”
based on a circular capacitor array (1024 caps per channel), 12 bit resolution
sampling frequency 5 GHz (200 ps) ® ~ 500 MHz (2 ns)
buffer depth 200 ns ® ~ 2 ms
several channels (up to 16) can be daisy chained ® 30 ms buffer depth
waveform stretcher
~ GHz sampling ® 30 MHz conversion ® 30 kHz readout (30 ms dead time)
needs frequent “re”calibration in time and energy + synchronization
E. cal
switch
diff. driver
analog front end
DRS
AD9222 12 bit
65 MHz
FPGA
trigger
LVDS
DRS4
global trigger bus
ch. 9
sinus wave
continuous T calibration and synchro
8 + 1 ch.
parallel
or serial ?

## Slide 8: DRS4 @ PSI http://drs.web.psi.ch
DRS4 Evaluation Board 4 channels 1-5 GSPS 12 bit
USB power
S. Ritt

## Slide 9
“Time stretcher” GHz  MHz

## Slide 10: Switched Capacitor Array
Shift Register
Clock
IN
Out
“Time stretcher” GHz  MHz
Waveform
stored
Inverter “Domino” ring chain
0.2 - 2 ns
FADC
33 MHz

## Slide 11: DRS Functional Block Diagram
IN
8 + 1 ch
OUT
CONTROLS
REFERENCE CLOCK

## Slide 12: Domino Wave Circuit (Digital Delay Line)
once the domino wave starts,
It continues indefinitely

## Slide 13: DRS Linearity
based on DRS 3
need accurate calibration
better if continous (ch. 9)
after “calibration”

## Slide 14: Performance – A detector
2011 studies in 2011 : Sasha, Oleg, Slava
same split signal
no delay
~ 15 ps
with delay
~ 35 ps
difference understood :
additional DRS time calibration required

## Slide 15: Performance – A Detector
~ 50 ps
~ 35 ps with improved algorithm

## Slide 16: Performance – ToF/L-R
rest with cosmic muons
result not so good
however:
intrinsic DRS resolution
discriminator (algorithm)
detector

## Slide 17: Performance tests
Plan extensive tests of the DRS system over the next two months
in particular
NA61 beam line with S1 (4 PMT’s,) + S2 + S4 (parasitically)
using available PSI test boards and CAEN modules
use several chips / boards -> synchronization of chips
Everybody welcome to join !

## Slide 18: Conceptual Layout (1)
clock
trigger
read
clear
busy
16 x in
16 x in
16 x in
16 x in
FPGA
OUT
data collector
16 x IN
4 DDL links
DDL
DRS board
DRS mother board (9U format)
serial
serial
define readout protocol
(DRS board ® data collector)
flexible enough for other applications

## Slide 19: Conceptual Layout (2)
DRS4
AD9222
8 ch ADC
33 MHz
12 bit
1 ch ADC
8 x in
sinus wave
clock ch 9
control
trigger
calib
FPGA
kintex 7
trigger
read
……..
1 Mbit
calibration
serial out
1 Gbit / s
control
EPROM
clock
x 2 (16 + 2 ch)
ch 9
DAC

## Slide 20: Overall structure
tentative design : 16 channels / DRS board board = 16 ch
64 channels / DRS mother board
ToF-L + ToF-F(L) (56 + 5 boards @ 5 GHz) DDL
ToF-R + ToF-F(R) (56 + 5 boards @ 5 GHz) DDL
PSD (28 boards @ 1 GHz) DDL
BPD (9 boards @ 0.5 GHz)
DDL
Beam (2 boards @ 5 GHz)
Beam (scalers, registers) VME
~ 2600 channels + spares
combine discriminator (CFD), ADC (multihit !), and TDC (multihit !) in a single module
i.e. remove CFDs, splitters, TDCs, ADCS, …
add multihit capabilities

## Slide 21: Location of DRS electronics
close to detectors or counting house ?
everything depends on trigger latency !
NOW : common start DRS : common stop
inside : remove cable delays, ??? ns
add trigger distribution, ??? ns
very likely not enough time to locate DRS electronics close to ToF
outside : delay trigger by ~ 200 ns
use more selective trigger than S1 (i.e. the FS already available)
to reduce data rate, read out only first 100 ns
S1
ToF gate ~ 100 ns
ToF gate ~ 200 ns
S1

## Slide 22: Proposal (work in progress)
Prepare DAQ readout upgrade proposal based on the DRS by next coll. meeting,
i.e. < 08.10.12 ! (if we agree to continue in this direction …)
[everybody is welcome and encouraged to contribute]
0. motivation / justification
1. conceptual design
(don’t need to work out details at this stage, i.e. how the clocks will be distributed, …)
2. implementation plan
3. implications for DAQ
4. costing (current ~100 CHF / ch, ~ 5k CHF / board, ~ 300 kCHF overall)
5. resources (human)
6. time scale
development (hardware, firmware, software) and production
installation and commissioning
7. backup plan
The system must be ready by 01.07.14 (restart of SPS)
(i.e. installed, tested, debugged, … w/o beam)

## Slide 23: Resources Required
1 engineer (1 FTE x 1.5 y) to develop DRS boards
(hardware and firmware)
1 engineer (1 FTE x 0.75 y) to develop DRS mother boards and DDL link
(hardware and firmware)
1 engineers / physicists (1 FTE x 1 y) to develop FPGA algos
(baseline subtraction and zero suppression, data encoding, synchronization …)
1 physicist (1FTEx 1 y) to develop calibration procedures and FPGA algos
(T and E calibration, waveform processing, …)
1 physicist (1 FTE x 1 y) DAQ modifications (i.e. include DRS)
1 physicist (1 FTE x 1 y) DAQ upgrade (i.e. prepare for vertex detector, etc.)
1 physicist (1 FTE x 0.5 y) VME readout
2 physicist (1 FTE x 1.5 y) offline / online modifications
(decoding, waveform processing, calibrations, QA, …)
TOTAL 10 FTEs x 1 y (or 5 FTEs x 2 y)

## Slide 24: Resources Required (2)
1 engineer (1 FTE x 1.5 y) to develop DRS boards
(hardware and firmware)
S. Debieux and D. LaMarra (UniGE)
1 engineer (1 FTE x 0.75 y) to develop DRS mother boards and DDL link
(hardware and firmware)
T. Kiss (Budapest) ???
1 engineers / physicists (1 FTE x 1 y) to develop FPGA algos
(baseline subtraction and zero suppression, data encoding, synchronization …)
T. Tolyhi (Budapest) ???
1 physicist (1 FTE x 1 y) to develop calibration procedures and FPGA algos
(T and E calibration, waveform processing …)
E. Kaptur (UniSilesia) + 0.5 FTE (>= PostDoc) ???
1 physicist (1 FTE x 1 y) DAQ modifications
(i.e. include DRS in DAQ stream) Andras + ???
1 physicist (1 FTE x 1 y) DAQ upgrade
(i.e. prepare for vertex detector, etc.) Andras + ???
1 physicist (1 FTE x 0.5 y) VME readout ???

## Slide 25: Timelines
Ready by June 2014
All debugging and commissioning w/o beam completed by June 2014
Dec 2012
study DRS performance (time resolution)
complete specifications (incl. detector interfaces and cabling)
start building prototype (full chain : DRS -> DDL -> PC) -> March ‘13
full implementation plan
explore implications for DAQ
explore implications for analysis
March 2013
complet prototype (full chain : DRS -> DDL -> PC)
start debugging prototype -> Sept ‘13
start developping waveform analysis (offline) -> March ‘14
June 2013
debug prototype -> Sept ‘13
finalize design
basic firmware (data transfer, DRS and ADC controls, calibrations)
start developping calibration algorithms -> June ‘14
plan DAQ modifications
start preparing for installation / backward compatibility -> June ‘14

## Slide 26: Timelines (2)
Sept 2013
external review
NA61 final decision
full working system with several DDL links
version 2 prototype
start developping data encoding and filtering (firmware) -> June ‘14
start developping calibration algorithms (firmware) -> June ‘14
start DAQ implementaiton -> June ‘14
Dec 2013
full funding available
complete DRS boards debugging and design
ready for mass production
all components in hand
basic DAQ ready
basic complete firmware ready
March 2014
all DRS boards procured
all DRS boards tested
complete preparations for installation
backward compatibility

## Slide 27: Timelines (3)
June 2014
system fully operational and debugged w/o beam
DAQ ready
analysis (offline) ready
July 2014
system fully debugged w/ beam
ready for physics